Given the continuity equation:
{partial q_x} over {partial x } + {partial q_y} over {partial y } + {partial h} over {partial t } = Pe
Where
qx	=	discharge per unit width on x-axis (m2/s)
qy	=	discharge per unit width on y-axis (m2/s)
h	=	flow depth (m)
Pe	=	effective rainfall rate (m/s)
The discharge is related to the head using manning equation, where (for either direction):
V = 1 over n R ^{ 2 over 3 } sqrt{ S } , R = A over P , and q = h.V
Where
V	=	flow velocity (at direction of flow) (m/s)
n	=	Manning roughness coefficient (m1/6)
R	=	hydraulic radius (m)
S	=	Energy slope, taken equal to the ground slope in the Kinematic wave	approximation (m/m)
A	=	flow cross-section (m2)
P	=	wetted parameter (m)
To simplify the Manning equation, a wide-channel assumption is made, in which the width of flow is assumed so large – relative to flow depth – that the hydraulic radius approximately equals the depth. The unit discharge then becomes:
q = h left( 1 over n h ^{ 2 over 3 } sqrt{ S }right)
Substituting in the continuity equation:
{partial } over {partial x } left[ h left( 1 over n h ^{ 2 over 3 } sqrt{ S_x }right)right] + {partial} over {partial y }left[ h left( 1 over n h ^{ 2 over 3 } sqrt{ S_y }right)right] + {partial h} over {partial t } = Pe

An issue becomes evident in that the space variable (h) is non-linear. To work around this, the velocity term 1 over n h ^{ 2 over 3 } sqrt{ S } is assumed constant (within an element), and the system is solved by iteration. Where the head is assumed only to compute the velocity, the entire equation is solved for the head, then the assumed and computed heads are compared, should they be significantly different, another iteration takes place where the computed head from the previous iteration is used to compute the velocity in the new iteration.
To this end, we keep the equation in the form:
{partial (u.h)} over {partial x } + {partial (v.h)} over {partial y } + {partial h} over {partial t } = Pe
Where u and v are the velocity components in x and y direction respectively. And since they are constants
u {partial h} over {partial x } + v {partial h} over {partial y } + {partial h} over {partial t } = Pe , or u {partial h} over {partial x } + v {partial h} over {partial y } + {partial h} over {partial t } - Pe = 0

To construct a finite elements approximate solution, the method of weighted residuals dictate that the exact solution of the problem h be replaced with an approximate solution tilde h , substituting the approximate solution in the equations above yield a residual instead of zero. This residual is forced globally to zero by multiplying the equation with a weighting function and integrating over a domain discretized to a finite number of elements. In other words:
iint from{%OMEGA} W_i left(u_i {partial tilde h} over {partial x } + v_i {partial tilde h} over {partial y } + {partial tilde h} over {partial t } - Pe right) d%OMEGA = R approx 0
Where Ω represents the domain, R is the residual, and Wi is the weight function.
The relationship between the approximate and exact solutions is defined in a piece-wise fashion, in the following form:
tilde h = sum from{nodes per element} { N_i h }
Where Ni is the shape function. An interpolation function that produces 1 at the position of its node and 0 on the other nodes, but may vary between 0 and 1 between the element’s nodes. For this application, the natural coordinate system is used as a shape function,
N_i = L_i , N_j = L_j , N_k = L_k

for a linear triangular (3 nodes) element, the relationships between the natural coordinates and the global, Cartesian coordinates are given by:

L_i = 1 over { 2A^e } left[ (x_j y_k - x_k y_j) + (y_j - y_k) x + (x_k - x_j) y right] newline L_j = 1 over { 2A^e } left[ (x_k y_i - x_i y_k) + (y_k - y_i) x + (x_i - x_k) y right] newline L_k = 1 over { 2A^e } left[ (x_i y_j - x_j y_i) + (y_i - y_j) x + (x_j - x_i) y right]
Where the e superscript denotes the element, the i, j, and k subscripts denote each specific node of this element. Substituting these relations in the approximate solution (for a linear triangle) yields:
tilde h = L_i h_i + L_j h_j + L_k h_k
And taking the partials with respect to x:
{partial tilde h} over {partial x} = {partial L_i h_i}over {partial x} + {partial L_j h_j}over {partial x} + {partial L_k h_k}over {partial x}
Note that the exact solution is constant within the element (fixed at the node), therefore {partial h}over {partial x} = 0 , the derivative of the approximate solution then becomes:
{partial tilde h} over {partial x} = h_i{partial L_i}over {partial x} + h_j{partial L_j }over {partial x} + h_k{partial L_k }over {partial x}
{partial tilde h} over {partial x} = 1 over {2A^e} left[ h_i (y_j - y_k) + h_j (y_k - y_i) + h_k (y_i - y_j) right]
And similarly for the y direction:
{partial tilde h} over {partial y} = 1 over {2A^e} left[ h_i (x_k - x_j) + h_j (x_i - x_k) + h_k (x_j - x_i ) right]
Plugging those derivatives in the main integral:
iint from{%OMEGA} N_i left[ u_i over {2A^e} left(h_i (y_j - y_k) + h_j (y_k - y_i) + h_k (y_i - y_j ) right) + v_i over {2A^e} left( h_i (x_k - x_j) + h_j (x_i - x_k) + h_k (x_j - x_i) right) + {partial tilde h} over {partial t } - Pe right] d%OMEGA newline{} = R approx 0
Note that the weight function Wi is replaced with the shape function Ni, as dictated by the Galerkin technique.
For brevity, take yij to denote (yi – yk), xji for (xj – xi), and so forth, then rearrange the terms.
iint from{%OMEGA} N_i left[ u_i over {2A} left(h_i y_jk + h_j y_ki + h_k y_ij right) + v_i over {2A} left( h_i x_kj + h_j x_ik + h_k x_ji right) + {partial tilde h} over {partial t } - Pe right] d%OMEGA = R approx 0
iint from{%OMEGA} N_i left[ h_i over {2A} (u_i y_jk + v_i x_kj ) + h_j over {2A} (u_i y_ki + v_i x_ij) + h_k over {2A} (u_i y_ij+ v_i x_ji) + {partial tilde h} over {partial t } - Pe right] d%OMEGA = R approx 0
For a 2 dimensional triangle, a simplified solution to the integral above is given by Segerlind 1984 (via Istok, 1989) as:
int from{A^e} { (N_i^e)^a (N_j^e)^b (N_k^e)^c} dA = { a! b! c! } over { (a + b + c + 2)!} 2A^e
Ergo:
left( {1!0!0!} over {(1 + 0 + 0 + 2)!} 2 A^e right) left[ h_i over {2A} ( u_i y_jk + v_i x_kj ) + h_j over {2A} (u_i y_ki + v_i x_ik) + h_k over {2A} (u_i y_ij+ v_i x_ji) - Pe right] +iint from{%OMEGA} { N_i {partial tilde h} over {partial t }} d%OMEGA approx 0
h_i over 6 ( u_i y_jk + v_i x_kj ) + h_j over 6 (u_i y_ki + v_i x_ik) + h_k over 6 (u_i y_ij+ v_i x_ji) - A^e over 3 Pe +iint from{%OMEGA} { N_i {partial tilde h} over {partial t }} d%OMEGA approx 0
Disregarding the time derivative for now, the last equation can be written in a shorthand form as:
[ K ]"{" h "}" - "{" %beta "}" Pe
Where [K] is the element’s conductance matrix, {h} is a vector for the heads at each node, {β} is a vector to the element’s precipitation contribution to a specific node. [K] and {β} given as:
[K] = 1 over {6} left[matrix { (u_i y_jk + v_i x_kj) # (u_i y_ki + v_i x_ik) # (u_i y_ij + v_i x_ji) ## (u_j y_jk + v_j x_kj) # (u_j y_ki + v_j x_ik) # (u_j y_ij + v_j x_ji) ## (u_k y_jk + v_k x_kj) # (u_k y_ki + v_k x_ik) # (u_k y_ij + v_k x_ji) }right] and {%beta} = A^e over 3 left[matrix { 1 ## 1 ## 1 }right]
For the time derivative term, two approaches are available to form the solution, the lumped formulation and the consistent formulation. In both, the term eventually reduces – similarly to the spatial derivative – to [C]"{" dot h "}" , [C] is called the capacitance matrix, given by (Istok, 1989):
[C_Lumped] = A^e over 3 left[matrix { 1 # 0 # 0## 0# 1 #0 ## 0 # 0 #1 }right] or [C_Consistent] = A^e over 12 left[matrix { 2 # 1 # 1 ## 1 # 2 # 1 ## 1 # 1 # 2 }right]
"{" dot h "}" is still a time derivative, to solve it a finite difference (in time) scheme is used, giving (Istok, 1989):
"{"h"}" = ( 1- %omega) "{"h"}"_t + %omega "{"h"}"_{ t + %DELTA t }
Where ω is a relaxation factor that determines the exact scheme used (forward, backwards or central in time). The entire approximate solution thus becomes:
[C] left( "{"h_{t+%DELTA t}"}" - "{"h_t"}" right) = - %DELTA t [ K ] left( (1 - %omega) "{"h_t"}" + %omega "{"h_{t+%DELTA t}"}" right) + %DELTA t "{"%beta"}" left( (1 - %omega) Pe_t + %omega Pe_{t+%DELTA t} right)
Where the t subscript denotes the value at the current time-step, and t+Δt subscript denotes the value at the next time-step.
Reorganizing the terms to have future (unknown) values on the left hand side and current (known) values on the right (note that the precipitation remains on the right even for future values as both are known):
[C] "{"h_{t+%DELTA t}"}" + %omega %DELTA t [ K ] "{"h_{t+%DELTA t}"}" = [C] "{"h_t"}" - %DELTA t (1 - %omega)[ K ] "{"h_t"}" + %DELTA t"{"%beta"}" left( (1 - %omega) Pe_t + %omega Pe_{t+%DELTA t} right)
left[ [C] + %omega %DELTA t [ K ] right] "{"h_{t+%DELTA t}"}" = left[ [C] - %DELTA t(1 - %omega)[ K ] right] "{"h_t"}" + %DELTA t"{"%beta"}" left( (1 - %omega) Pe_t + %omega Pe_{t+%DELTA t} right)
To reiterate, solving the above equation requires assuming – future – nodal head values to compute the velocities, which go into the conductance matrix [K]. The equation then reduces to a linear system of equations of the form [ A ] "{"x"}" = "{"b"}" , where [A] is the component left[ [C] + %omega %DELTA t [ K ] right] , {x} are the unknown, future, nodal heads, "{"h_{t+%DELTA t}"}" , and {b} is the resultant of the right hand side left[ [C] - %DELTA t[ K ] (1 - %omega) right] "{"h_t"}" + %DELTA t"{"%beta"}" left( (1 - %omega) Pe_t + %omega Pe_{t+%DELTA t} right) , which comprises entirely of known values. The resulting heads are compared to the assumed ones, reiterating again if the difference is unacceptable.