Starting from
{partial q_x} over {partial x } + {partial q_y} over {partial y } + {partial h} over {partial t } = Pe

Constructing the integral by moving all terms to one side, multiplying by the weighting function (Taken as shape function, Galerking method), and integrating over the whole domain, yields a residual that is close to zero.

iint from{%OMEGA} {N_i({partial tilde q_x} over {partial x } + {partial tilde q_y} over {partial y } + {partial tilde h} over {partial t } - Pe)d%OMEGA} = R approx 0

Or

R = iint from{%OMEGA} {N_i({partial tilde q_x} over {partial x } + {partial tilde q_y} over {partial y } - Pe)d%OMEGA} newline + iint from{%OMEGA} {N_i{partial tilde h} over {partial t }d%OMEGA}

The approximate solution for qx at an element is the sum of the actual qx at each node multiplied by the interpolation function at that node, or:

tilde q_x = sum from{nodes per element} { N_i q_x }

For 2d elements, we take the interpolation function equal to the natural coordinate, or:

N_i = L_i , N_j = L_j , N_k = L_k

For triangular elements, the natural coordinates can be transformed to the global coordinate system using:
L_i = 1 over { 2A^e } left[ (x_j y_k - x_k y_j) + (y_j - y_k) x + (x_k - x_j) y right] newline L_j = 1 over { 2A^e } left[ (x_k y_i - x_i y_k) + (y_k - y_i) x + (x_i - x_k) y right] newline L_k = 1 over { 2A^e } left[ (x_i y_j - x_j y_i) + (y_i - y_j) x + (x_j - x_i) y right]

Or in matrix form:

[L] = 1 over { 2A^e } left[ matrix { (x_j y_k - x_k y_j) # (y_j - y_k) x # (x_k - x_j) y ## (x_k y_i - x_i y_k) # (y_k - y_i) x # (x_i - x_k) y ## (x_i y_j - x_j y_i) # (y_i - y_j) x # (x_j - x_i) y }right]

The approximate solution for qx thus becomes:

{partial tilde q_x} over {partial x} = { partial (N_i q_i + N_j q_j + N_k q_k)} over {partial x }

{partial tilde q_x} over {partial x} = q_xi over { 2A^e } ( y_j - y_k ) + q_xj over { 2A^e } ( y_k - y_i ) + q_xk over { 2A^e } ( y_i - y_j )

And similarly for qy
{partial tilde q_y} over {partial y} = q_yi over { 2A^e } (x_k - x_j) + q_yj over { 2A^e } ( x_i - x_k ) + q_yk over { 2A^e } ( x_j - x_i )

At node i, both Nj and Nk = 0, therefore:
R_i " "= " " iint from{%OMEGA} L_i left( q_xi over { 2A^e } ( y_j - y_k ) + q_yi over { 2A^e } (x_k - x_j) - Pe right) d%OMEGA " " + " " iint from{%OMEGA} {N_i{partial tilde h} over {partial t }d%OMEGA}

Similarly, at nodes j and k:
R_j " " = " " iint from{%OMEGA} L_j left( q_xj over { 2A^e } ( y_k - y_i ) + q_yj over { 2A^e } (x_i - x_k) - Pe right) d%OMEGA " " + " "iint from{%OMEGA} {N_j{partial tilde h} over {partial t }d%OMEGA}

R_k " " = " " iint from{%OMEGA} L_k left( q_xk over { 2A^e } ( y_i - y_j ) + q_yk over { 2A^e } (x_j - x_i) - Pe right) d%OMEGA " " + " " iint from{%OMEGA} {N_k{partial tilde h} over {partial t }d%OMEGA}

Take the first Term of Ri
iint from{%OMEGA} L_i left( q_xi over { 2A^e } ( y_j - y_k ) + q_yi over { 2A^e } (x_k - x_j) - Pe right) d%OMEGA
Using Segerlind 1984 formula (via Istok 1989),

int from{A^e} { (N_i^e)^a (N_j^e)^b (N_k^e)^c} dA = { a! b! c! } over { (a + b + c + 2)!} 2A^e

The integral then evaluates to
iint from{%OMEGA} L_i left( q_xi over { 2A^e } ( y_j - y_k ) + q_yi over { 2A^e } (x_k - x_j) - Pe right) d%OMEGA = ({ 1! 0! 0! } over { (1 + 0 + 0 + 2)! } 2A^e) left( q_xi over { 2A } ( y_j - y_k ) + q_yi over { 2A } (x_k - x_j) - Pe right)

{} = 1 over 6 q_xi ( y_j - y_k ) + 1 over 6 q_yi (x_k - x_j) - A^e over 3 Pe

Similarly for other nodes

1 over 6 q_xj ( y_k - y_i ) + 1 over 6 q_yj (x_i - x_k) - A^e over 3 Pe

1 over 6 q_xi ( y_i - y_j ) + 1 over 6 q_yi (x_j - x_i) - A^e over 3 Pe

Or in shorthand for the three nodes:
[%PSI_x] "{"q_x"}" + [%PSI_y] "{"q_y"}" - "{"%beta"}""{"Pe"}"
Where qx, qy, Pe and β are vectors, and Ψx and Ψy are matrices. β, Ψx and Ψy are defined as:
[%PSI_x] = 1 over {6} left[matrix { (y_j - y_k) # (y_k - y_i) # ( y_i - y_j ) ## (y_j - y_k) # (y_k - y_i) # ( y_i - y_j ) ## (y_j - y_k) # (y_k - y_i) # ( y_i - y_j ) }right]

[%PSI_y] = 1 over {6} left[matrix { (x_k - x_j) # (x_i - x_k) # (x_j - x_i) ## (x_k - x_j) # (x_i - x_k) # (x_j - x_i) ## (x_k - x_j) # (x_i - x_k) # (x_j - x_i) }right]

[%beta] = A^e over {3} left[matrix {1 ## 1 ## 1 }right]

For the time integral, we use the lumped formulation, where the (element) capacitance matrix is given by (Istok, 1989):
[C] = A over 3 left[matrix { 1 # 0 # 0 ## 0 # 1 # 0 ## 0 # 0 # 1 }right]

(Note: In the work of Keesara and Eldho used as reference, the consistent formulation was used).

The entire equation thus becomes:
[R] =[%PSI_x] "{"q_x"}" + [%PSI_y] "{"q_y"}" - "{"%beta "}" "{"Pe"}" + [C]"{"h"} " approx 0

To account for time derivative, we introduce variable ω and modify the equation so as to have
{partial h} over { partial t } = ( 1 - %omega ) h_t + %omega h_{ t+%DELTA t }
Or:
matrix{ [R] #{}={}# {}#[%PSI_x] left( (1 - %omega) "{"q_x"}"_{t} + %omega "{"q_x"}"_{t + %DELTA t} right) ## {}#{} #{}+{}# [%PSI_y] left((1 - %omega) "{"q_y"}"_{t} + %omega "{"q_y"}"_{t + %DELTA t} right) ## {}#{} #{}-{}# "{"%beta "}" left((1 - %omega) {Pe}_{t} + %omega {Pe}_{t + %DELTA t} right) ## {}#{} #{}+{}# 1 over {%DELTA t}[C]left("{"h"}"_{t + %DELTA t} - "{"h"}"_t right) ## {}#{} #{}approx{}# 0 }

Reordering to have {h}t+Δt on the LHS:

matrix { [C]"{"h"}"_{t + %DELTA t} # {}={} # {} # [C]"{"h"}"_t ## {}#{}# {}-{} # %DELTA t[%PSI_x] left( (1 - %omega) "{"q_x"}"_{t} + %omega "{"q_x"}"_{t + %DELTA t} right) ## {}#{}# {}-{} # %DELTA t[%PSI_y] left((1 - %omega) "{"q_y"}"_{t} + %omega "{"q_y"}"_{t + %DELTA t} right) ## {}#{}# {}+{} # %DELTA t "{" %beta "}" left((1 - %omega) {Pe}_{t} + %omega {Pe}_{t + %DELTA t} right) }